## Slide 1
Brain Tumor Segmentation on FPGA
with Adaptive Processing Mode Selection
Digital System Design Lab
Board: Nexys A7-100T (Artix-7 xc7a100tcsg324-1)
Tools: Vitis HLS / Vivado 2025.1

## Slide 2
Problem Statement
Brain tumor segmentation from MRI is critical for diagnosis
Software-only approaches are slow and power-hungry
Goal: FPGA acceleration for real-time, energy-efficient processing
Input: 256×256 grayscale MRI images
Target: Nexys A7-100T (Artix-7, 100 MHz)

## Slide 3
Novelty – Adaptive Mode Selection
Image Quality | Mode | Behaviour
High contrast | FAST | Minimal processing, max speed
Medium contrast | NORMAL | Standard Otsu + cleanup
Low contrast | CAREFUL | Adaptive threshold + full morph

## Slide 4
System Architecture
MicroBlaze CPU ←AXI→ HLS Otsu Accelerator
Shared 128 KB Image BRAM (dual-port, dual AXI BRAM controllers)
AXI SmartConnect merges HLS gmem0/gmem1 → BRAM
Peripherals: UART (115200), GPIO (5 LEDs), Timer
MicroBlaze controls pipeline; HLS does heavy computation

## Slide 5
Algorithm Pipeline
1. Histogram – 256-bin grayscale histogram (II=1, pipelined)
2. Otsu Threshold – maximise inter-class variance
3. Morphology – erode/dilate for noise removal (mode-dependent)
4. Adaptive Mode – auto-select FAST/NORMAL/CAREFUL from image stats
5. Watershed – connected-component labelling (software post-processing)

## Slide 6
Implementation Flow
Phase 1: Python – Verify algorithm (Otsu + Watershed + metrics)
Phase 2: HLS C++ – Synthesise Otsu to IP core (xc7a100tcsg324-1)
Phase 3: Vivado – Build MicroBlaze SoC + bitstream
Phase 4: Vitis – MicroBlaze bare-metal firmware
Phase 5: Test Images – Convert PNG → .bin / .h
Phase 6: Documentation – Report, presentation, user manual

## Slide 7
HLS Synthesis Results
Step | Status | Details
C Simulation | ✅ PASSED | All 9 tests, all 3 modes
C Synthesis | ✅ 97 MHz | II=1 on all major loops
IP Export | ✅ Generated | custom_hls_otsu_threshold_top_1_0.zip

## Slide 8
FPGA Resource Usage (Estimated)
Resource | Used | Available | Utilisation
LUT | 30,969 | 63,400 | 48%
FF | 33,247 | 126,800 | 26%
BRAM_18K | 168 | 270 | 62%
DSP | 163 | 240 | 67%

## Slide 9
Segmentation Results
Image | Dice Score | Mode Selected
brain_01 (bright tumor) | 0.98 | FAST
brain_02 (subtle tumor) | 0.98 | NORMAL
brain_03 (no tumor) | 0.19 | CAREFUL

## Slide 10
Performance Comparison: SW vs FPGA
Metric | SW (Python/CPU) | HW (FPGA) | Improvement
Otsu time | ~20 ms (MB) | ~3.4 ms (best) | ~5.9× speedup
Power | 200 mW | 50 mW | 4× lower
Energy per image | ~4,000 µJ | ~169 µJ | ~95.8% savings

## Slide 11
Demo
Live demo on Nexys A7-100T board
Serial terminal (115200 baud) shows processing results
LEDs indicate current processing mode and status:
  LD0: Heartbeat
  LD1: Processing active
  LD2-LD3: Mode (00=FAST, 01=NORMAL, 10=CAREFUL)
  LD4: Done

## Slide 12
Conclusion
✅ Successfully implemented Otsu segmentation on FPGA
✅ Adaptive mode selection – novel contribution
✅ ~5.9× speedup, ~95.8% energy savings (SoC-fair baseline)
✅ Complete pipeline: Python → HLS → Vivado → Vitis
Future Work:
  Higher resolution (512×512+)
  DMA-based data transfer for faster I/O
  Real MRI DICOM image support
  Zynq port with ARM + Linux

## Slide 13
Thank You!
Questions?
github.com/akulasahasra75/FPGA--Brain-Tumor-Segmentation